## Slide 1: Module-2 Line Encoding

## Slide 2
DIGITAL-TO-DIGITAL CONVERSION
In this section, we see how we can represent digital data by using digital signals. The conversion involves three techniques: line coding, block coding, and scrambling. Line coding is always needed; block coding and scrambling may or may not be needed.
Topics discussed in this section:
Line Coding
Line Coding Schemes Block Coding

## Slide 3
Line coding is the process of converting digital data to digital signals. We assume that data, in the form of text, numbers, graphical images, audio, or video, are stored in computer memory as sequences of bits.
Line coding and decoding
LINE CODING

## Slide 4
LINE CODING . . .

## Slide 5
Signal Element Versus Data Element :
Goal is to send data elements. Data element is the smallest entity that can represent a piece of information: this is the bit.
A signal element carries data elements. A signal element is the shortest unit (time wise) of a digital signal.
Data elements are what we need to send; signal elements are what we can send. Data elements are being carried; signal elements are the carriers.
LINE CODING SCHEMES CHARACTERISTICS
We define a ratio r which is the number of data elements carried
by each signal element.
Signal element versus
data element

## Slide 9
Solution
A signal is carrying data in which one data element is encoded as one signal element ( r = 1). If the bit rate is 100 kbps, what is the average value of the baud rate if c is between 0 and 1?
Solution
We assume that the average value of c is 1/2 . The baud rate is then

## Slide 10
Effect of lack of Synchronisation
A self-synchronizing digital signal includes timing information in the data being transmitted. This can be achieved if there are transitions in the signal that alert the receiver to the beginning, middle, or end of the pulse. If the receiver' s clock is out of synchronization, these points can reset the clock.

## Slide 11
LINE CODING SCHEMES

## Slide 12
UNIPOLAR
All signal levels are on one side of the time axis - either above or below.
NRZ - Non Return to Zero scheme is an example of this code. The signal level does not return to zero during a symbol transmission.
Scheme is prone to baseline wandering and DC components. It has no synchronization or any error detection. It is simple but costly in power consumption.

## Slide 13
The voltages are on both sides of the time axis.
Polar NRZ scheme can be implemented with two voltages. E.g. +V for 1 and -V for 0.
There are two versions:
  NZR - Level (NRZ-L) - positive voltage for one symbol and negative for the other
  NRZ - Inversion (NRZ-I) - the change or lack of change in polarity determines the value of a symbol. E.g. a “1” symbol inverts the polarity a “0” does not.
POLAR - NZR

## Slide 14
POLAR NZR – L and NRZ – I SCHEMES

## Slide 15
In NRZ-L the level of the voltage determine the value of the bit.
In NRZ-I the inversion or the lack of inversion determines the value of the bit.
Note
NRZ-L and NRZ-I both have an average signal rate of N/2 Bd.
NRZ-L and NRZ-I both have a DC component problem and baseline wandering, it is worse for NRZ-L.
Both have no self synchronization &no error detection. Both are relatively simple to implement.

## Slide 16
POLAR RZ SCHEME
The Return to Zero (RZ) scheme uses three voltage values. +, 0, -.
Each symbol has a transition in the middle. Either from high to zero or from low to zero.
This scheme has more signal transitions (two per symbol) and therefore requires a wider bandwidth.
No DC components or baseline wandering.
Self synchronization - transition indicates symbol value.
More complex as it uses three voltage level. It has no error detection capability.

## Slide 17
POLAR RZ SCHEME

## Slide 18
Manchester coding consists of combining the NRZ-L and RZ schemes.
  Every symbol has a level transition in the middle: from high to low or low to high. Uses only two voltage levels.
Differential Manchester coding consists of combining the NRZ-I and RZ schemes.
  Every symbol has a level transition in the middle. But the level at the beginning of the symbol is determined by the symbol value. One symbol causes a level change the other does not.
POLAR – BIPHASE : MANCHESTER AND DIFFERENTIAL MANCHESTER

## Slide 19
POLAR – BIPHASE : MANCHESTER AND DIFFERENTIAL MANCHESTER
SCHEMES

## Slide 20
Note
In Manchester and differential Manchester encoding, the transition at the middle of the bit is used for synchronization.
The minimum bandwidth of Manchester and differential Manchester is 2 times that of NRZ. The is no DC component and no baseline wandering. None of these codes has error detection.

## Slide 21
Code uses 3 voltage levels: - +, 0, -, to represent the symbols (note not transitions to zero as in RZ).
Voltage level for one symbol is at “0” and the other alternates between + & -.
Bipolar Alternate Mark Inversion (AMI) - the “0” symbol is represented by zero voltage and the “1” symbol alternates between +V and -V.
Pseudoternary is the reverse of AMI.
POLAR – AMI AND PSEUDOTERNARY

## Slide 22
POLAR – AMI AND PSEUDOTERNARY