## Slide 1: Chapter 7
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
ARP and RARP

## Slide 2: Outline
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
ARP
ARP Package
RARP
The McGraw-Hill Companies, Inc., 2000

## Slide 3: Logical Addresses
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
The hosts and routers are recognized at the network level by their logical addresses
  A logical address is an internet address
  Called a logical address because it is usually implemented in software
  The logical addresses in the TCP/IP are called IP address and are 32 bits long

## Slide 4: Physical Address
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
However, hosts/routers are recognized at the physical layer by their physical address
  A physical address is an local address
  Called a physical address because it is usually implemented in hardware
  Examples
 48-bit MAC addresses in Ethernet

## Slide 5: Translation
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
We need both the physical address and the logical address for packet delivery
Thus, we need to be able to map a logical address to its corresponding physical address and vice versa
Solutions
  Static mapping
  Dynamic mapping

## Slide 6: Static Mapping
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Create a table that associates a logical address with a physical address and store in each machine
However, physical addresses may change
  A machine could change its NIC resulting in a new physical address
  In some LANs, such as LocalTalk, the physical address changes every time the computer is turned on
  A mobile station can move from one physical network to another, resulting in a change in its physical address

## Slide 7: Dynamic Mapping
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Use a protocol to find another address
ARP: Address Resolution Protocol
  Map a logical address to a physical address
RARP: Reverse Address Resolution Protocol
  Map a physical address to a logical address

## Slide 8: ARP and RARP
F
igure 7-1 | 
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 9: Position of ARP and RARP in TCP/IP Protocol Suite
F
igure 7-2
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 10
A R P
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
7.1

## Slide 11: ARP Operation
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
To find the physical address of another host or router on its network
  Send an ARP request message
ARP request message
  The physical address of the sender
  The IP address of the sender
  The physical address of the receiver is 0s
  The IP address of the receiver

## Slide 12: ARP Operation (Cont.)
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Then, ARP request message is broadcast by the physical layer
  For example: in Ethernet, MAC header’s destination address is all 1s (broadcast address)
  Received by every station on the physical network
The intended recipient send back an ARP reply message
  ARP reply message packet is unicast

## Slide 13: ARP Operation
F
igure 7-3
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 14: ARP Packet
F
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
igure 7-4

## Slide 15: Packet Format
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
HTYPE (Hardware type)
  16-bit field defining the underlying type of the network
    Ethernet is given the type 1
    ARP can be used on any physical network
PTYPE (Protocol type)
  16-bit field defining the protocol
 IPv4 is 080016
    ARP can be used with any higher-level protocol

## Slide 16: Packet Format (Cont.)
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
HLEN (Hardware length)
  8-bit field defining the length of the physical address in bytes
    Ethernet has the value of 6
PLEN (Protocol length)
  8-bit field defining the length of the logical address in bytes
    IPv4 has the value of 4
OPER (Operation)
  16-bit field defining the type of packet
  (1) = ARP request, (2) = ARP reply

## Slide 17: Packet Format (Cont.)
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
SHA (Sender hardware address)
  A variable-length field defining the physical address of the sender
SPA (Sender protocol address)
  A variable-length field defining the logical address of the sender

## Slide 18: Packet Format (Cont.)
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
THA (Target hardware address)
  A variable-length field defining the physical address of the target
  For an ARP request operation packet
 This field is all 0s
TPA (Target protocol address)
  A variable-length field defining the logical address of the target

## Slide 19: Encapsulation of ARP Packet
F
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
igure 7-5
An ARP packet is encapsulated directly into a data link frame
Type field indicates that the data carried by the frame is an ARP packet
The McGraw-Hill Companies, Inc., 2000

## Slide 20: Operations
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
The sender knows the target’s IP address
IP asks ARP to create an ARP request message
  The sender physical address
  The sender IP address
  The target physical address field is filled with 0s
  The target IP address
The message is passed to the data link layer to encapsulate in a data link frame
  Physical destination address is broadcast address

## Slide 21: Operations (Cont.)
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Every host or routers receives the frame and since the destination address is broadcast, pass it to the ARP
  All machines’ ARP except the one targeted drop the packet
The target reply with an ARP reply message that contains its physical address and is unicast
The sender receives the reply message and knows the target’s physical address

## Slide 22: Four Cases to Use ARP
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Case 1: The sender is a host and wants to send a packet to another host on the same network
  Use ARP to find another host’s physical address
Case 2: The sender is a host and wants to send a packet to another host on another network
  Sender looks at its routing table
  Find the IP address of the next hop (router) for this destination
  Use ARP to find the router’s physical address

## Slide 23: Four Cases Using ARP: Case 1
F
igure 7-6:a
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 24: Four Cases Using ARP: Case 2
F
igure 7-6:b
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 25: Four Cases to Use ARP (Cont.)
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Case 3: the sender is a router and received a datagram destined for a host on another network
  Router check its routing table
  Find the IP address of the next router
  Use ARP to find the next router’s physical address
Case 4: the sender is a router that has received a datagram destined for a host in the same network
  Use ARP to find this host’s physical address

## Slide 26: Four Cases Using ARP: Case 3
F
igure 7-6:c
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 27: Four Cases Using ARP: Case 4
F
igure 7-6:d
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 28
An ARP request is broadcast;
an ARP reply is unicast.
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 29: Example 1
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
A host with IP address 130.23.43.20 and physical address 0xB23455102210
Another host with IP address 130.23.43.25 and physical address 0xA46EF45983AB.
The two hosts are on the same Ethernet network
Show the ARP request and reply packets encapsulated in Ethernet frames

## Slide 30: Solution
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Figure 7.7 shows the ARP request and reply packets
Note that
  The IP addresses are shown in hexadecimal

## Slide 31: Example 1
F
igure 7-7: request
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 32: Example 1 (Continued)
F
igure 7-7: reply
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 33: Proxy ARP
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Used to create a subnetting effect
A router running a proxy ARP
  Its ARP acts on behalf of a set of hosts
  If it receives an ARP request message looking for the address of one of these host
    The router sends an ARP reply announcing its own hardware (physical) address
  After the router receives the actual IP packet
    It sends the packet to the appropriate host or router

## Slide 34: Example
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
Administrator need to create a subnet without changing the whole system
Add a router running a proxy ARP

## Slide 35: Proxy ARP
F
igure 7-8
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 36
RARP
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
7.3

## Slide 37: RARP
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
A diskless machine is usually booted from ROM
It cannot include the IP address
  IP address are assigned by the network administrator
Obtain its logical address by the physical address using the RARP protocol

## Slide 38: RARP Operation
F
igure 7-10
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 39
The RARP request packets are broadcast;
the RARP reply packets are unicast.
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com

## Slide 40: Packet Format
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
The format of the RARP packet is the same as the ARP packet
Except that the operation field is
  Three for RARP request message
  Four for RARP reply message

## Slide 41: RARP Packet
F
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
igure 7-11

## Slide 42: Encapsulation of RARP Packet
F
The McGraw-Hill Companies, Inc., 2000
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
igure 7-12

## Slide 43: Alternative Solutions to RARP
PDF created with FinePrint pdfFactory Pro trial version www.pdffactory.com
When a diskless computer is booted, it needs more information in addition to its IP address
  The subnet mask
  The IP address of a router
  The IP address of a name server
RARP cannot provide this extra information
Two protocols, BOOTP and DHCP, can be used instead of RARP